## Slide 1: Use Case 13
Lab 3: Epileptic Seizure Detection
Winter School 25/01/2022

## Slide 2
Contents
Epilepsy Detection
Dataset
Recurrent approach
Convolutional approach
Resources
23
13
7
3
29

## Slide 3: Epilepsy Detection

## Slide 4
Epilepsy Detection
Introduction
Epilepsy
  Neurological disorder characterized by recurrent seizures
  Episodes of involuntary movement
  Around 50 million people diagnosed in the world
Electroencephalogram (EEG)
  Recording the electrical activity of the brain
  Electrodes located on the scalp
  Continuous signal composed by different channels

## Slide 5
Epilepsy Detection
Brain stages
Interictal
Normal activity.
Pre-ictal
Strange brain activity. Usually before an actual seizure.
Ictal
Period while a patient is suffering a seizure.
Post-Ictal
The patient is recovering from a seizure.

## Slide 6
Epilepsy Detection
Brain Stages
General cycle of stages
Automatic seizure detection task (not prediction few minutes before seizures)
High variability between subjects
  Patient-Dependent classifiers
Class 0
Interictal + Pre-ictal + Post-ictal
Class 1
Ictal
Notes: High variability: Normal activity for one patient could be abnormal for another one -> The high variability makes it difficult the task -> Patient-Dependent approach: One classifier per patient.

## Slide 7: Dataset

## Slide 8
CHB-MIT Scalp EEG Database from Physionet
EEG recordings from 24 pediatric subjects
Data in EDF (European Data Format)
Sessions are between 24 and 48 hours long, split in several files
Most files are 1 hour long, others are longer (up to four hours)
Electrodes located on the scalp (10-20 system standard)
23 channels, related to pairs of electrodes
Captured at 256 Hz
Manual Labelling: Starting and Ending times of seizures
Dataset
Data description

## Slide 9
Dataset
Data description
Notes: Here we can see a 10 seconds extract of a signal from the dataset. At the left side, we can observe the labels for the channels. As you can see, each channel refers to two electrodes.

## Slide 10
Preparation preprocess (Data cleaning process done by Winter-School team):
  Read signals from EDF format
  Homogenize signals to have each channel in the same position
  Store the data in a Python dictionary (containing signals and seizure information)
  Serialize the object in Pickle to save it (.pbz2 files)
We provide a subset of the original dataset already cleaned
Dataset
Data preparation, cleaning and selection
clean_signals/
chb01/
chb03/
chb05/
…

## Slide 11
Dataset
Splits
65 %
Train
15 %
Validation
20 %
Test
31,2 hours
7,2 hours
9,6 hours
A whole session of 48 hours
Splits not in chronological order

## Slide 12
Dataset
Class imbalance
Seizures normally last few seconds, so there is a high class imbalance.
Patient id | # files without seizures | # files with seizures | # interictal hours | # ictal hours
chb01 | 35 | 7 | 40,43 | 0,12
chb03 | 31 | 7 | 37,89 | 0,11
chb05 | 34 | 5 | 38,85 | 0,16
chb08 | 15 | 5 | 19,75 | 0,26
chb12 | 11 | 10 | 20,41 | 0,28
chb14 | 19 | 7 | 25,95 | 0,05
chb15 | 25 | 14 | 38,46 | 0,55
chb24 | 10 | 12 | 21,15 | 0,14
Total | 180 | 67 | 242,89 | 1,67

## Slide 13: Recurrent Approach

## Slide 14
Recurrent Neural Networks
  LSTM / GRU layers
Data Loader
Post inference process
Metrics
  Neural Network Metrics
  Post inference Metrics
Results
Recurrent Approach
Introduction

## Slide 15
Recurrent Approach
RNN topologies based on LSTM and GRU layers
Recurrent Layer
Input shape: (19, 256)
In the first example provided we are using 19 timesteps of one-second-long sliding windows, that is why the input shape is (19, 256). Because each one of the 23 channels is processed independently.
256 units
(256,)
Dense Layer
Output Layer
256 units
(256,)
0 - Interictal
1 - Ictal
1 unit
(timesteps = 19, data_dim = 256)

## Slide 16
Recurrent Approach
Data Loader
Data Loader Sequence Parameters
  window_length (in seconds)
  shift (in seconds)
  timesteps

## Slide 17
Recurrent Approach
Data Loader - Example
Example of sequence generation
  window_length = 1 second
  shift = 0.5 seconds
  timesteps = 19
(19, 256)
(19, 256) x 23
When using all the 23 channels

## Slide 18
Recurrent Approach
Data Loader - Example
Input shape: (19, 256)
(19, 256) x 23
We independently pass each channel through the net
Training Mode
0 - Interictal
1 - Ictal
RNN
Model
RNN
Model
RNN
Model
RNN
Model
x 23
RNN
Model
RNN
Model
RNN
Model
Input Tensor
x 23
19
256
Inference Mode
Classification by consensus
0 - Interictal
1 - Ictal
RNN
Model

## Slide 19
Recurrent Approach
Post inference process
Post inference function to act as a detector
  Analyses the consecutive outputs
  Raises alarms when it detects a seizure
Post-Inference window
... 0 0 0 0 1 0 0 0 0 1 1 1 1 1 1 1 0 1 1 0 0 0 0 0 1 1 0 1 0 0 0 0 ...
Prediction
If the proportion of ones inside the post-inference window while being in the Interictal state is greater than alpha_pos, it makes the transition from Interictal to Ictal: T.0.1
If the proportion of ones inside the post-inference window while being in the Ictal state is lower than alpha_neg, it makes the transition from Ictal to Interctal: T.1.0
... 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 1 0 0 0 0 0 0 0 0 0 0 0 0 0 ...
Ground Truth
Inference window length
Detection threshold

## Slide 20
Recurrent Approach
Post-inference window accuracy
Percentage of detected seizures
Average Latency (in seconds)
False Alarms per hour
Metrics
Accuracy
Macro F1-score
Balanced Accuracy
Classifier Metrics
Post Inference process Metrics
Metrics at two levels
  Channel independent
  Ensemble: all 23 channels combined

## Slide 21
Recurrent Approach
Results
Experiment configuration
Window Length (s) | Shift (s) | Timesteps | Model | Optimizer | Initial LR | Epochs
1 | 0,5 | 19 | GRU | Adam | 0,0001 | 10
Post-Inference Parameters
Post-Inference Window Length (in timesteps) | Alpha_pos | Alpha_neg | Detection Threshold (s)
20 | 0,4 | 0,4 | 20

## Slide 22
Recurrent Approach
Results
 | Test |  |  |  |  |  | Post-Inference Process with Test subset |  |  |  |  | 
 | Channel Independent |  |  | Combined channels |  |  | Acc | # Seizures | Detected seizures | Latency (s) | False Alarms per Hour | Hours
Patient | Acc | F1-Score | Balanced Acc | Acc | F1-score | Balanced Acc |  |  |  |  |  | 
chb01 | 99,75% | 0,8828 | 86,34% | 99,93% | 0,9667 | 94,45% | 99,90% | 2 | 100,00% | 11,75 | 0,00 | 9,62
chb03 | 99,62% | 0,6117 | 57,53% | 99,64% | 0,4991 | 50,00% | 99,64% | 2 | 0,00% | - | 0,00 | 8,97
chb05 | 99,75% | 0,8553 | 87,35% | 99,90% | 0,9335 | 88,46% | 99,87% | 1 | 0,00% | - | 0,13 | 7,98
chb08 | 97,60% | 0,7215 | 83,11% | 99,49% | 0,9054 | 87,71% | 99,49% | 1 | 100,00% | 18,00 | 0,80 | 4,99
chb12 | 95,26% | 0,5774 | 63,09% | 97,63% | 0,6018 | 58,85% | 97,53% | 11 | 54,55% | 13,92 | 2,67 | 5,98
chb14 | 99,76% | 0,5856 | 58,21% | 99,85% | 0,5252 | 51,32% | 99,85% | 2 | 0,00% | - | 0,00 | 6,98
chb15 | 96,70% | 0,6383 | 67,83% | 97,86% | 0,6363 | 61,32% | 97,71% | 7 | 28,57% | 11,75 | 1,89 | 8,98
chb24 | 99,34% | 0,7385 | 69,23% | 99,49% | 0,7586 | 67,56% | 99,44% | 4 | 100,00% | 11,50 | 0,16 | 6,28

## Slide 23: Convolutional Approach

## Slide 24
Time Delay Convolutional Neural Networks
Post Inference Process
Metrics
  Neural Network Metrics
  Post inference Metrics
Results
Convolutional Approach
Introduction

## Slide 25
Convolutional Approach
Time Delay Convolutional Neural Networks
Kernel_size = (128, 23), strides = (64, 1) --> 500 ms long window shifted every 250 ms
Input shape: (2560, 23)

## Slide 26
Convolutional Approach
Models available in the pipeline
  "Conv1"
Post Inference Process
Metrics
  Neural Network Metrics
  Post inference Metrics

## Slide 27
Convolutional Approach
Results
Experiment configuration
Window Length (s) | Shift (s) | Model | Optimizer | Initial LR | Epochs
10 | 0,25 | Conv1 | Adam | 0,00001 | 10
Post-Inference Parameters
Post-Inference Window Length (in timesteps) | Alpha_pos | Alpha_neg | Detection Threshold (s)
20 | 0,4 | 0,4 | 20

## Slide 28
Convolutional Approach
Results
 | Test |  |  | Post-Inference Process with Test subset |  |  |  |  | 
Patient | Acc | F1-score | Balanced Acc | Acc | # Seizures | Detected seizures | Latency (s) | False Alarms per Hour | Hours
chb01 | 99,72% | 0,8940 | 96,15% | 99,69% | 2 | 100,00% | 9,00 | 0,73 | 9,62
chb03 | 99,62% | 0,8086 | 91,86% | 99,56% | 2 | 100,00% | 2,88 | 1,78 | 8,98
chb05 | 99,66% | 0,8330 | 92,07% | 99,59% | 1 | 0,00% | - | 1,76 | 7,98
chb08 | 99,2% | 0,8477 | 81,74% | 99,19% | 1 | 100,00% | 16,75 | 1,80 | 4,99
chb12 | 96,73% | 0,5530 | 55,63% | 96,51% | 11 | 45,45% | 15,90 | 7,52 | 5,98
chb14 | 98,83% | 0,4971 | 49,49% | 98,71% | 2 | 0,00% | - | 4,01 | 6,98
chb15 | 97,63% | 0,7848 | 94,28% | 97,52% | 7 | 57,14% | 10,44 | 3,01 | 8,98
chb24 | 99,22% | 0,6435 | 60,05% | 99,23% | 4 | 75,00% | 9,25 | 0,96 | 6,28

## Slide 29: Resources

## Slide 30
Resources
Original Dataset
Prepared Dataset
Pipeline Repository
clean_signals.zip (XX GB)
CHB-MIT Scalp EEG Database
UC13_pipeline

## Slide 31
Javier Martínez Bernia
jamarbe2@prhlt.upv.es
Thank you!